## Slide 1: RFI Group 2: Geocentric Mission Concepts
Ira Thorpe – NASA/GSFC
For the Group #2 Evaluation Team
Tyson Littenberg
Bob Spero
Gary Welter
Pete Bender
Jeff Livas
Tuck Stebbins

## Slide 2: Group 2 Mission Concepts
Acronym | Lead Author | Concept | Arm Length (Mkm) | Duration (yrs) | # alternates
GEOGRAWI | Tinto | Triangle from 3 geostationary SC, spherical proof mass | 0.07 | 2? | 3
GADFLI | McWilliams | Triangle from 3 geostationary SC | 0.07 | 2 | 3
OMEGA | Hellings | 6 micro-SC in 600,000km Earth-Moon orbit | 1.04 | 3 | 1
LAGRANGE | Conklin | 3 SC in Earth-Moon L3,L4,L5 Single optical bench, spherical proof mass | 0.67 | 5 | 1

## Slide 3: Sensitivity Curves
*NOTE: These curves are taken directly from the RFI. Ongoing attempts to reconcile them with calculated curves indicate their may be some significant discrepancies.

## Slide 4: BH Science I
Horizon distance for BH waveforms:
  “PhenomC” waveforms (IMR, no higher harmonics)
  Mass ratio = 1:3, spin1 = spin2 = ½, SNR = 10
NWNH: Measurements of BH mass and spin will be important for understanding the significance of mergers in the building of galaxies.
Notes: Add text for fiducial system. Which waveforms? (IMR, PhenomC, 22-only) Add LISA

## Slide 5: BH Science 2
BH Detection Rates
  Convolve horizon with population models (SC,SE,LC,LE)
  S = Small Seeds, L = Large Seeds, C = Chaotic Spin Evolution, E = Efficient Spin Evolution
  Detections “come with” precision measurements of mass and spin
NWNH: Measurements of BH mass and spin will be important for understanding the significance of mergers in the building of galaxies.
Notes: Which waveforms? – PhenomC (IMR, 22 only)

## Slide 6: EMRI Science
Horizon distance for EMRIs:
  Barack-Cutler waveforms
  10 Msun compact object, eccentricity = 0.5, 2 years before plunge
  Central black hole with spin = ½, Threshold SNR = 15.
Total # of detections over mission lifetime:
  Observation times: 5 yrs (Conklin), 3 yrs (OMEGA), 2 yrs (GeoStationary)
  EMRI population a (conservative) variant of Class.Quant.Grav. 21 (2004) S1595-S1606
NWNH: Detections of signals from EMRIs would provide exquisitely precise tests of Einstein’s theory of gravity.
Notes: Add LISA Horizon. Understand event rates.

## Slide 7: Galactic Binary Science
Andromeda Galaxy
Virgo Cluster
Magellanic Clouds
10 – 10 Msun Binary System, Threshold SNR = 7
0.5 – 0.5 Msun Binary System, Threshold SNR = 7
WD-WD Detections from Nelemans Catalog
Number of known verification binaries w/ SNR > 7
Notes: What are stellar mass BHBH rates? Better labels on plots

## Slide 8: Discovery Space
Discovery Space
  Measure of volume of signal space accessible to discover:
  Normalized by LISA volume
NWNH: Potential for discovery of waves from unanticipated or exotic sources.
Notes: What are stellar mass BHBH rates? Better labels on plots

## Slide 9: Science Summary
NWNH identified goals:
  All concepts will provide some information on mass & spin of MBH. Event rates are higher with OMEGA & LAGRANGE and higher SNR should also improve parameter estimation
  OMEGA & LAGRANGE have high probability of detecting EMRIs. It is not likely GEOGRAWI or GADFLI will detect EMRIs.
  OMEGA & LAGRANGE have a discovery volume 3-10x larger than GEOGRAWI or GADFLI
Other LISA Science (Galactic Binaries)
  All concepts detect compact binaries
  No verification binaries with GEOGRAWI or GADFLI
OMEGA and LAGRANGE concepts significantly out-perform the geostationary concepts in all science metrics

## Slide 10: Orbits
Concept | Arm variation (%) | Interior Angle variation (deg) | Range Rate (m/s)
GEOGRAWI/GADFLI | .02 | .02 | 1
OMEGA | .1 | 12 | 160
LAGRANGE | .05 | 5 (20) | 150 (360)
SGO-High | .01 | 0.8 | 13
GEOGRAWI/GADFLI provide a much more stable constellation.
Station keeping needed for LAGRANGE
6-SC design of OMEGA mitigates interior angle change
Single-bench design of LAGRANGE exacerbates interior angle change

## Slide 11: Mission Design
Concept | LV C3 (km/s)2 | PM ∆v (m/s) | Cruise duration (months)
GEOGRAWI/GADFLI | -9.0 | 1 | 4
OMEGA | -1.6 | 500 | 13
LAGRANGE | -1.7 | 800 | 7-9
SGO-High | 0.3 | 1100 | 14
GEOGRAWI/GADFLI orbits are less costly to reach than OMEGA/LAGRANGE
GEOGRAWI/GADFLI may be able to use micro-thrusters for orbit insertion
GEOGRAWI/GADFLI also require de-orbit or boost into graveyard orbit after science operations. May still require PM

## Slide 12: Sun Angle & Eclipses
Concept | In-plane Orbital Period (days) | Annual solar elevation change (deg) | Biannual Eclipse Season Duration (days) | Eclipses / Season
GEOGRAWI/GADFLI | 1 | 23.5 | 40 | 120
OMEGA | 55 | 5 | 14 | 0.75
LAGRANGE | 30 | 5 | 21 | 2
Thermal fluctuation period compared with measurement band
Loss of signal during eclipse & recovery time
There will be an “exposure season” centered in the eclipse season when the Sun-link angle becomes small. This will require some mitigation strategy.

## Slide 13: Technology Development
Gravitational Reference Sensor
  GADFLI baselines LPF GRS, highest TRL within group
  GEOGRAWI & LAGRANGE baseline spherical proof mass, technology development effort needed to raise TRL
  OMEGA baselines modified ONERA accelerometer. Concern that LPF GRS (37kg) may not fit in mass budget (80kg SC)
Sun filter
  ALL of these concepts require a strategy to mitigate Sun pointing events.
  OMEGA specifies a filter that appears to meet optical performance. Concern with scaling to large size and maintaining pathlength stability.
  Other strategies could be a shutter or re-pointing
Micro-Thrusters
  Station-keeping for LAGRANGE
  Orbit insertion and decommissioning for GADFLI/GEOGRAWI
  Low mass, power, volume for OMEGA

## Slide 14: Risk Pro/Cons
OMEGA
  Con: Aggressive use of micro satellite architecture. May preclude heritage from LPF due to size/mass.
  Pro: 6 SC arrangement provides redundancy
LAGRANGE:
  Con: Single proof mass per SC and redundancy

## Slide 15: Recommendation
A majority of group members support recommending OMEGA as the Group 2 concept to undergo a Team-X study.
A dissenting minority recommended LAGRANGE