## Slide 1: SGO Low: A LISA-like gravitational wave observatory with four links
Ira Thorpe – NASA/GSFC
For the SGO Core Concept Team
Submitted in Response to NASA RFI #NNH11ZDA019L

## Slide 2: Overview
Design Goal: Reduce LISA measurement concept to minimum four-link design while retaining primary science targets.
Architecture: Four “identical” SC in 1Gm triangle, each with one payload assembly
Two “corner” SC compare laser phase via 10km free-space link

## Slide 3: Design Parameters
Arm Length: 1Gm
Opening Angle: 60o
Orbit: Heliocentric drift-away at ~9o behind Earth
Displacement sensitivity: 18x10-12 m/Hz1/2
Residual Acceleration Noise: 3x10-15 m/s2/Hz1/2
Science Operations Duration: 2 years

## Slide 4: Projected Sensitivity
Above ~30mHz, sensitivity is equal or better than SGO High
Below ~10mHz, instrumental sensitivity is ~10x worse
No significant contribution from galactic foreground
Sensitive to all three classes of LISA astrophysical sources

## Slide 5: Measurement Performance
Massive Black Hole Binaries
  Detect ~12/yr with SNR ~ 100
  median z ~ 5, max z ~ 12
  Masses/spins ~ few %
  Distance ~ 20%
  Sky Location ~ 80deg2
Extreme Mass Ratio Inspirals
  Detect ~20/yr @ z < 0.15
  Masses/Spins ~ 10-4
Galactic Binaries
  ~2x103 resolved sources
  7 verification binaries
  Sky location ~ few deg

## Slide 6: Science Performance
Understand the formation of massive black holes
  Not likely to directly detect seed BH
  May constrain seed population by observing their progeny
Trace the growth and merger history of massive black holes and their host galaxy (NWNH)
  By measuring mass/spin and rough redshift of MBH mergers, BH growth is traced
  EMRI’s give very precise measurements in local universe
  Sky localization insufficient for identifying host galaxy
Explore stellar populations and dynamics in galactic nuclei
  EMRI events help characterize immediate environments of MBH in the local universe
  Some risk that no EMRI’s are detected if pessimistic event rate estimates are assumed

## Slide 7: Science Performance - Continued
Survey compact stellar-mass binaries and study the structure of the galaxy
  Few thousand individual binaries with measured mass & spin will provide information on the demographics of compact objects in the Milky Way.
Confront General Relativity with observations
  Compare MBH waveforms with numerical relativity
  Map spacetime of individual MBH with EMRI and compare to Kerr solution (NWNH)
  Compare EM and GW observations of galactic binaries
Probe new physics and cosmology, and search for unforseen sources of gravitational waves (NWNH)
  Limited by four-link design, which does not allow cross-checks

## Slide 8: Instrument Design
Simplifications from SGO High / LISA
  Single GRS per SC, 12-DOF control system
  No Optical Assembly Tracking Mechanism
  Reduced laser power (0.7W)
  Reduced telescope size (25 cm)
  No on-board frequency reference (arm-locking)
  UV-LED charge control
  Reduced point-ahead angle and angle rate
  Reduced component count
Additional Components
  8 cm back-link telescope with tip/tilt control

## Slide 9: Spacecraft Design

## Slide 10: Mission Design
Launch Stack
  Each SC mates with propulsion module
  Four SC/PM pairs stack in fairing
  Total wet stack mass of ~4300kg
Launch Vehicle Possibilities
  Atlas V (531), 650kg margin
  Falcon 9 Heavy, 9200kg margin. Shared launch?
Trajectory:
  Direct insertion into drift-away
  Total Δv ~ 130m/s
Orbit Stability
  ΔL/L ~ 0.6%, Doppler ~ 2 MHz, interior angle variation ~ 0.6o

## Slide 11: Cost Estimate
Basis
  LISA Project costs from multiple epochs
  LISA Pathfinder development costs
  LV cost data
  70% success probability and 20% reserves
  Credit taken for non-recurring engineering costs
ROM Cost Estimate: $1.41B (FY12)

## Slide 12: Schedule
Phase |  | Duration (months)
A |  | 12
B |  | 30
C/D |  | 66
E | transfer | 18
 | commissioning | 4
 | Science ops | 24
Schedule based on LISA project schedule with some savings during I&T and operations
9 years pre-launch, 22 months transfer & commissioning, 2 years operations
Extended mission limited by constellation stability & communication

## Slide 13: Summary
The SGO Low concept addresses 2 of the 3 science priorities for space-based gravitational wave detection identified in the NWNH report.
Low technical risk due to heritage from LISA Pathfinder and past LISA technology development and risk-reduction activities.
No cost savings relative to SGO Mid despite moderate loss of science performance
Small cost savings relative to SGO High with significant loss of science performance

## Slide 14: SGO Core Concept Team