## Slide 1: Interferometer in Space for Detecting Gravity Wave Radiation using Lasers (InSpRL) Dec-21-2011 Workshop on Gravity Wave Detection
Presenter: Babak . N . Saif

## Slide 2: InSpRL Team
Gravitational-Wave Mission RFI
Submitted by: Dr. Babak N. Saif, Instrument PI, GSFC Optics Branch, Babak.n.saif@nasa.gov, 301-286-5433
Study Team: Marcel Bluth, ATK Boom Engineer, Marcel.Bluth@atk.com
Lee D. Feinberg, GSFC Chief Large Optics Systems Engineer, Lee.D.Feinberg@nasa.gov
Dr. Peter Graham, Professor of Physics, Stanford University, PWGraham@stanford.edu
Dr. Jason Hogan, Department of Physics, Stanford University, Hogan@stanford.edu
Dr. Leo Hollberg, Prof. Physics, Stanford and Chief Technology Officer (Consulting) AOSense, Inc., leoh@stanford.edu
Dr. Mark Kasevich, Prof. Physics and Applied Physics, Stanford University, kasevich@stanford.edu
Dr. Ritva Keski-Kuha, GSFC Optical Engineer, Ritva.a.keski-kuha@nasa.gov
Dr. John Mather, GSFC Senior Astrophysicist, John.C.Mather@nasa.gov
M. Bruce Milam, GSFC Aerospace Manager, Bruce.Milam@nasa.gov
Dr. Surjeet Rajendran, Physicist, Stanford, Rajendran@stanford.edu
Charles Perrygo, Genesis, Senior Mechanical Systems Engineer, charles.m.perrygo@nasa.gov
Bernard D. Seery, GSFC Assistant Director for Advanced Concepts, bernie.seery@nasa.gov
Dr. David Spergel, Senior Astrophysicist, Princeton University, dns@astro.princeton.edu

## Slide 3: Outline of the talk
Why Atom Interferometry to detect Gravity Waves?
Basics Of Atom Interferometer.
Atom Gradiometer as a sensor for detection of Gravity Wave.
Amplification of Gravity Wave Phase:
1) Large Momentum Transfer (LMT)
2) Resonance(Heterodyne) detection
Laser Phase Noise Mitigation
Proposed Configurations.
Phase calculation.
Existing Technologies and Technology Maturation

## Slide 4: Atom Interferometer Contributions
Why Atom Interferometry for Gravity Wave Detection???
A neutral atom is naturally decoupled from its environment. That makes atoms nearly ideal inertial test masses. This means they are ideally suited to measure Gravitational effects of all kinds including Gravity Wave.
Amplification of the Gravity Wave OPD(phase) due to Coherent
multiple interaction of light with the atom. AKA Large Momentum Beam Splitter.
This is a noiseless quantum mechanical amplification of Phase.
No Radiation Pressure Noise.
Amplification of the Gravity Wave Phase due to Resonance(heterodyne)
detections.

## Slide 5: An Atom and a Set of Three Pulses Create a Mach-Zahnder interferometer
g
g
e
g
e
Atom in Excited State
Atom in the Ground State
Time Axis
Spatial
Axis
A
B
C
D

## Slide 6: GW as a Gravity Gradient
GW is like a (time dependent) gravity gradient
Geodesic deviation looks the same for GW and gravity gradient
Gravity gradiometer can detect GWs
Freely-falling (LLF)
Gravitational field
Residual gravity gradient
We use a differential pair of atom interferometers to detect a GW
Each measures the local acceleration, resulting in a gravity gradiometer
Gravity gradient is analogous to a GW:

## Slide 7: Coherent Phase Amplification
Large momentum transfer (LMT) beamsplitters – multiple laser interactions
Each laser interaction adds a momentum recoil and imprints the laser’s phase
Example LMT interferometer
LMT energy level diagram
 Phase amplification factor N
Notes: Detuning
omegas

## Slide 8: Resonant Detection
Additional phase amplification possible with multiple loop atom trajectory
Q oscillations
T
Period T of atom oscillation matched to GW period, so each phase adds constructively.
 Phase amplification factor Q
(Vacuum)
(Spontaneous emission)
(Sunshield/boom length)
(Rabi frequency)
(Ta is LMT pulse duration)
dx
Constrained by ensemble lifetime and achievable atom kinematics:

## Slide 9: Phase Response Optimization
T
T
Constraints
Atom ensemble lifetime
Total interferometer time < 1000 s (Vacuum)
Acceleration time < 30 s (Spontaneous emission)
Kinematics
Spatial extent < 250 m (Boom length)
Max Acceleration < 300 m/s2 (Rabi frequency)
High frequency: f > 0.1 Hz
 Continuous acceleration
Low frequency: f < 0.1 Hz
 Drift and hold
Maximize spatial extent given maximum acceleration
Minimize spontaneous emission by limiting atom-light interaction time.

## Slide 10: Laser Phase Noise Mitigation
We have had discussions with members of CST and core team on laser
phase noise mitigation for our single arm geometries.
Our original RFI proposed method would require a stable laser oscillator.
While single arm configuration would be game changing, the above method needs further study and makes the comparison of our RFI response to others difficult.
Here we present two modified configurations to enable a direct comparison.

## Slide 11: Two proposed short baseline configurations enabled by atom interferometry
f = 1 Hz
N = 2000
Q =30
(sinusoidal)
High
Low
L = 500 m
f = 1 Hz
N = 2000
Q =30
(sinusoidal)
L = 500 km
f = 0.01 Hz
N = 2100
Q = 9
(10 s drift time,
30 s hold)
f = 0.01 Hz
N = 85
Q = 9
(10 s drift time,
30 second hold)
High
Low
 Scientifically interesting sensitivity possible with short baseline because of phase amplification factor of N*Q

## Slide 12: Simple derivation of sensitivity curves
Example:
L = 500 m
dx = 250 m
Max. wavepacket acceleration: 1 g
QT = 1000 s
SNR: 104:1/Hz1/2
RFI response contains fully constrained optimization subject to spontaneous emission and lattice depth.
GW metric(LLF):
Differential phase between two interferometers separated by L, with arms oscillating sinusoidally with amplitude dx due to the atom optics sequence:
Path integral phase shift:
GW potential:
(like a gravity gradient potential)

## Slide 13: Strain Sensitivity
L = 500 km
L = 500 m

## Slide 14: Existing Technology
Use 10 m prototype to evaluate atom optics sequences.
Can demonstrate methods at the h ~ 10-19/Hz1/2 level at 3 Hz (but blinded by seismic noise).
Collaboration with L. Hollberg for ultra-stable laser required for single-arm design.
AOSense commercial AI gravimeter
102 hk LMT atom optics demonstrated
10 m atom drop tower test facility
AOSense commercial Sr clock

## Slide 15: FY’ 12/13 Technology Maturation Activities
Technology | Descriptions | Lead Institution | TRL status | Facility
LMT | Higher Momentum Recoil | Stanford University | 3 | Stanford University 10 Meter Tower
WavePackets Coherence | Spatial Coherence over 10 meters | Stanford University |  | Stanford University 10 Meter Tower
Atom Source Engineering | Delta kick Cooling | Stanford University | 3 | Stanford University 10 Meter Tower
Laser | PSD Measurements of MOFA | GSFC | 5 | GSFC laser Lab
System Design | Over all System Design. Instruments, Orbit, Launch Vehicle,…… | GSFC | N/A | GSFC IDC/MDL
Boom Stability | ATK Boom Stability and dynamics | ATK | 4 | ATK Test Facility

## Slide 16: Backup Slides

## Slide 17: Example transfer functions
Spatial and temporal laser beam phase requirement vs. transverse spatial frequency.
Laser phase noise transfer function
Satellite jitter
……

## Slide 18: Example error model
Requires specialization to the proposed antenna geometries.

## Slide 19: SNR
SNR of 1.4x104 in 1 second demonstrated on Cs clock transition (Biedermann PhD, also Opt. Lett).
GW sensitivity curves derived assuming 104:1 in 1 second.
Gradiometer laser phase noise study (left to right: DBR, ECDL, cavity locked )
Phase shift as a function of applied frequency shift for middle interferometer pulse. Allows determination of baseline.

## Slide 20
Gravity gradiometer
Demonstrated accelerometer resolution: ~10-11 g. Operated on a truck.

## Slide 21: Optical Atomic “clock” serves as Phase Reference for Atom Interferometry
Do not require absolute frequency accuracy nor even reproducibility
Do not require operation as a “clock”
Do not require continuous measurements
Continuous operation could be benefit in some cases and is feasible
  Very short “fountain 1.25 cm for Tramsey= 100 ms; easy on ground
  Interleaved clouds of atoms
  Space operation even easier, atoms don’t fall, near 100% recapture
Do require outstanding frequency and phase stability
Do want synchronization with Atom Interferometry pulses
  Then laser frequency noise can be removed, dead time not an issue
  Optical cavity thermal noise will not limit performance

## Slide 22
Cold Atom Optical Clocks
    Atomic fractional frequency instability: (Allan deviation)
    Tcycle= time to measure both sides of atomic resonance
    TRamsey= Ramsey interrogation time
    Q = line quality factor = / C = fringe contrast
     = averaging time Natom= # of atoms detected in Tcycle
  For example: atomic stability feasible w/ Ytterbium (Sr, …)
     = 556 nm, 519 THz clock transition
     = 1/(2TRamsey) = 5 Hz , TRamsey =100 ms
    C = 30 %
    0 = 519 THz NA=108
    y = 3x10-18 in 200 ms
    y() = 1x10-18 -1/2 Tcycle = 4 TRamsey
Hollberg et al. IEEE, JQE 37 (2001)
y() = 1x10-19 -1/2 ?

## Slide 23
Ytterbium optical atomic clock
398.9 nm,
28 MHz
1P1 (6s6p)
3P1: 555.8 nm,
182 kHz
3P0,1,2 (6s6p)
- Excellent prospects for high stability and small absolute uncertainty
Energy
λ = 578 nm
Δν = ~0 174Yb
15 mHz 171Yb, 173Yb
1S0
Notes: Hot topic: evidence

## Slide 24
Ytterbium optical atomic clock
NIST, Boulder Chad Hoyt
Zeb Barber
Chris Oates
Jason Stalnaker
Nathan Lemke
398.9 nm,
28 MHz
1P1 (6s6p)
3P1: 555.8 nm,
182 kHz
3P0,1,2 (6s6p)
- Excellent prospects for high stability and small absolute uncertainty
Lattice
759 nm
Energy
λ = 578 nm
Δν = ~0 174Yb
15 mHz 171Yb, 173Yb
(171Yb, 173Yb I=1/2,5/2)
1S0
Notes: Hot topic: evidence