## Slide 1: Superconducting Antenna Concept for Gravitational Wave Radiation
A. Guliana (Presenter),
J. Foremanb, V. Nikoghosyana,c, S. Nussinova,d, L. Sicaa, J. Tollaksena
aChapman University, Schmid School for Science and Technology, Orange, CA & Burtonsville, MD
bIndependent Researcher, Alexandria, VA
cInstitute for Physics Research, National Academy of Sciences, Ashtarak, 0203, Armenia
dSchool of Physics and Astronomy, Tel-Aviv University, Ramat-Aviv, Tel-Aviv, Israel
ITAR Disclaimer: This presentation does not contain technical data per 22 CFR 120.10–distribution unrestricted w/o 3282.

## Slide 2
Executive Summary
A novel concept of superconducting GW antenna.
Non-resonant, applicable to wide spectrum of sources.
Highly sensitive: h0~10-26 at 102Hz; h0~10-23 at 102 mHz.
Moderate volume: 10 m lateral size.
Passive cooling below critical temperature of superconducting components far from the Sun.
Very little energy consumption at operation.
Easy to orient.
Virtually unrestricted operational time.

## Slide 3: Starting Point
Tidal force tends to accelerate back and forth from CG.
Exchange interaction prohibits ionic motion.
Coulomb interaction prohibits electronic motion.
L=Lh0sin t
L
m
m
Next step: metallic bar
+
+
Bimetallic bar, negative meff
e
e
g

## Slide 4
Next Step: Closing Current Trajectory
x2
x1
This design breaks
Coulomb blockade:
during two half-periods electrons will now move clockwise and counter-clockwise
Why superconductivity?

## Slide 5: Why Superconductivity
Motion of electrons in semiconductors and normal metals,
though sometimes called “free”, is Aristotelian:
it persists while the force is acting. Ohms law: j~v~eE~F,
v~F , i.e., velocity in response to force
In superconductors dv/dt~E, i.e., motion is Newtonian!
This difference has crucial consequences:
in S/C current response is greater by a factor ()-1 ~1010+.
Ten or more orders of magnitude more than justify SC.
Price to pay: no negative masses for SC. Cooper pairs have positive mass.

## Slide 6
What if mAeff > mBeff>0?
Tidal force is ~m0.
Acceleration ~meff-1.
Torque ~ nA(B), density of carriers.
Next Step Forward
x2
x1
Subject to electroneutrality (which imposes nAvA=nBvB, at S=const), the electric current is:
Here L –side length of antenna, S is its cross section.

## Slide 7
  At L=103cm, S=102cm2 the resultant current is about femtoampere for a wave with amplitude h0=10-26 and frequency 100 Hz. It will be the same for a given value of h0. For example, at 100mHz, 1 fA yields at h0~10-23, etc.
  This looks encouraging, however, there is still a problem we will address next.
Estimates of Antenna Response

## Slide 8
if meff~m0 , nB<<nA , and nB~1022cm-3 :
    Inductance (Magnetic Energy)
How to neutralize magnetic field?

## Slide 9
cross section
    “Spaghetti” Structure
layers with A and B swapped
Currents move in opposite directions and cancel the magnetic field.
The number of spaghetti depends
on geometry; large but realistic.

## Slide 10
At I=1 fA and R=5m, B=0I/(2R)~10-16 T.
SQUID noise floor 3fT/Hz1/2 : 10-17 T /1 day of measurement.
Freedom to exploit, say, 10 SQUIDs for different groups of layers, and/or get to weaker GW source detection, and/or reduce the observation time.
    Readout
R
B

## Slide 11
Noise Floor of the Detector
Real noise floor of this antenna is due to normal resistance
Two notes are important here:
at low T the normal fluid (and its influence) dies out exponentially;
bandwidth  can be made narrow for periodic signals (large integration time).
Our estimates indicate that achievable noise floor is about 10 fA/Hz1/2 , which inspires optimism.
In,IS

## Slide 12
We elaborated a novel concept of the GW antenna.
We see no showstopper for this concept and would
welcome experts opinion on its viability.
Hopefully, in parallel to other large-scale efforts, such
as the LIGO approach and LISA mission or NANO
gravitational initiative, the suggested concept will
become useful for one of the most challenging
experiments – the detection of gravitational waves.
We cannot build it, but NASA can!
Conclusions